## Slide 1
AI-DRIVEN ESTIMATION AUTOMATION
DRAWINGS
AI / VISION
ENGINEERING
QUANTITIES

## Slide 2
1. Construction Estimation Scope
Major construction materials / work categories identified with the Estimation Team
1. Concrete & Shuttering
HIGH PRIORITY | Current development Focus | Beam & Slab
2. Steel
HIGH PRIORITY | Current development Focus | Beam
3. Blockwork
Wall / block quantities
4. Tiles & Granite
Floor / wall finishes
5. Plastering
Internal / external surfaces
6. Painting
Paintable surfaces
7. Waterproofing
Wet areas / terraces
8. Doors & Windows
Openings / glazing
9. Earthwork
Excavation / filling quantities
10. Landscaping
Landscape / external works
11. Plumbing & Electrical
Plumbing / electrical works
12. MS Grill Work
Grill / metal fabrication works
Highlighted focus areas: High Priority - Steel & Concrete
AI Construction Estimation | 2

## Slide 3
2. Major Structural Components
The structural estimation framework is organized around these core components
1. Beam
Concrete ✓
Shuttering✓ Steel✓
Current development focus
2. Slab
Concrete ✓
Shuttering ✓
Steel
Current development focus
3. Column
4. Foundation
5. Shear Wall
6. Retaining Wall
Highlighted focus areas: High Priority - Beam & Slab
AI Construction Estimation | 3

## Slide 4
3. What Does Construction Estimation Involve?
From engineering information to measurable, reviewable quantities
INPUT
• Drawings
• Schedules
• Notes
• Revisions
INTERPRET & MEASURE
• Geometry
• Dimensions
• Areas
• Lengths
• Counts
CALCULATE
• Engineering rules
• Formulas
• Project practices
VALIDATE
• Quantity checks
• Anomalies
• Estimator review
OUTPUT
• Quantity take-off
• BOQ-ready data
• Excel
AI Model aims to reduces repetitive effort — engineering logic remains central to quantity calculation.
AI Construction Estimation | 4

## Slide 5
4. Current AI Development Focus
CONCRETE — BEAM & SLAB
• Beam concrete • Beam shuttering • Slab concrete • Slab shuttering • Deterministic calculation • LLM assistance for ambiguous inputs
STEEL — BEAM
• Reinforcement drawing understanding • Beam matching / ownership • Reinforcement parsing • Hybrid CAD + Vision • Deterministic engineering authority • Diameter wise Steel Calculations
• Steel quantity + BBS
AI Construction Estimation | 5

## Slide 6
5. Concrete Beam & Slab — Estimation Architecture
Concrete Beam & Slab Model
http://13.201.15.89
DXF FRAMING DRAWING
Drawing input
DETERMINISTIC CAD / GEOMETRY PIPELINE
Member detection • Geometry • Dimensions • Areas / lengths
LLM ASSISTANCE — WHEN NEEDED
Missing / ambiguous inputs → slab thickness • tags • beam dimensions • bounded regions
STANDARD DRAWINGS
Processed deterministically from the DXF
AMBIGUOUS INFORMATION
LLM assists only where drawing information is unclear
ENGINEERING INTERPRETATION
Combine geometry + resolved inputs
DETERMINISTIC ENGINEERING ENGINE
Rules • formulas • quantity calculations • validation
BEAM CONCRETE + SHUTTERING
Concrete volume • shuttering area
SLAB CONCRETE + SHUTTERING
Concrete volume • shuttering area
EXCEL QUANTITY REPORT
Review sheet • flagged items
Design principle: Standard inputs → deterministic calculation | Ambiguous inputs → LLM assistance → deterministic calculation
AI Construction Estimation

## Slide 7
6. Concrete POC - Estimation Team Validation
1
ACCURACY
Current Model Performance
2
PRODUCTIVITY
Time Reduction
3
WHAT THIS MEANS
Key Takeaways
Comparison with manual estimation (Estimation Team)
Work Item
Concrete Accuracy
Shuttering Accuracy
Beam
78%
81%
Slab
69%
73%
Reduction in time required for quantity take-off (compared to manual method)
Beam
67%
time saving
Slab
29%
time saving
PROCESSING EFFORT REDUCED
Automation delivers clear time savings for quantity take-off.
ACCURACY STILL REQUIRES IMPROVEMENT
Current quantities are not yet accurate enough for direct use.
MANUAL VERIFICATION IS CURRENTLY REQUIRED
Results need to be reviewed and corrected by the Estimation Team.
POC CONCLUSION
Automation demonstrated considerable time savings; however, current accuracy requires further development and manual verification before production use.
AI Construction Estimation | 8

## Slide 8
7. Steel Beam — Hybrid Estimation Architecture
DXF DRAWING
DETERMINISTIC CAD GEOMETRY PIPELINE
CAD geometry • Beam geometry • Span / engineering facts
CLAUDE / VISION PIPELINE
Context + Detail View → Claude Vision → Semantic Reinforcement
ENGINEERING FACTS
Geometry • cover • spacers • lengths
VISION INTERPRETATION
Bar count • diameter • main/extra • stirrups
HYBRID RESOLUTION
Combine vision + engineering facts
DETERMINISTIC ENGINEERING ENGINE
Rules • calculations • quantities • validation
CUT LENGTH + DL
PIECE GENERATION
STEEL QUANTITY
BBS
EXCEL
AI Construction Estimation

## Slide 9
9. End-to-End Steel Estimation Workflow
1.
Upload drawing package
2.
Understand drawing
3.
Extract geometry & context
4.
Identify components / material regions
5.
Route to estimation engine
6.
AI / Vision where required
7.
Hybrid resolution
8.
Deterministic quantity calculation
9.
Validation & review
10.
BOQ / BBS / Excel
AI Construction Estimation | 10

## Slide 10
10. Steel Beam — Internal Accuracy Testing
Current model testing result • Subject to Estimation Team validation
Steel Beam Estimation Model
http://13.127.104.99/
Beam BBS — Automation vs Estimated
Inizio 9th framing
All quantities in KGS
Description
UOM
8
10
12
16
20
25
32
Total
Estimated / Manual
KGS
1,561.1
9,375.2
9,171.8
2,871.9
12,026.0
22,638.4
1,152.0
58,796.3
Automated
KGS
931.1
3,917.6
2,599.0
3,374.8
10,205.7
13,794.8
1,185.3
36,008.4
Difference in quantity
KGS
630.0
5,457.6
6,572.7
502.9
1,820.3
8,843.5
33.4
22,787.9
Error Scale
Underestimate
Underestimate
Underestimate
Overestimate
Underestimate
Underestimate
Overestimate
Underestimate
% Accuracy
-
60%
42%
28%
82%
85%
61%
97%
61%
Key Observations from Estimation Team
01
BAR DIAMETER
Top bars specified as 16 mm in the drawing are sometimes read as 20 mm in the output.
02
STIRRUPS
Number of stirrups calculation is incorrect in some cases.
03
SPACER BARS
Spacer diameter and quantity are not consistently taken as per General Notes; same spacer bar may be counted twice.
04
BEAM SIZE
Beam length is not always as per the framing plan, causing slight underestimation.
AI Construction Estimation | Steel Beam

## Slide 11
Cropped Beam Image Sent to Claude
Estimation Team Interpretation
Claude/ Hybrid Answer
Steel Beam

## Slide 12
Cropped Beam Image Sent to Claude
Estimation Team Interpretation
Claude/ Hybrid Answer
Steel Beam

## Slide 13
Estimation Team Interpretation
Cropped Beam Image Sent to Claude
Claude/ Hybrid Answer
Steel Beam

## Slide 14
Why Estimation Automation Takes Significant Time
Development effort varies by work item • Engineering understanding + diagnostics + validation
1. Engineering Complexity
Different drawings, structural rules, quantity logic and calculation methods for each work item.
2. Drawing Understanding
Understand how information is represented, connected and interpreted in real construction drawings. This must be transferred to the System.
3. Root-Cause & Diagnostics
Trace incorrect results through multiple stages to identify the actual source of the problem.
4. Solution & Iteration
Implement possible solutions and test them across different drawing conditions and edge cases.
5. Validation & Reliability
Validate outputs against engineering expectations before the automation can be trusted.
Development time = Understanding → Diagnosis → Solution → Iteration → Validation
AI Construction Estimation | Development

## Slide 15
https://www.youtube.com/watch?v=zX3IDPlJeR8